## Slide 1: Rig Notes: Vibration Test (Synthetic)
Test type: impact/ringdown on a cantilever beam mounted to a rigid fixture
Objective: estimate the first 3 modal frequencies and damping ratios
  Deliverables: zeta via (i) log decrement (time-domain) and (ii) half-power bandwidth (FFT)

## Slide 2: Sensor Mounting & Axis Mapping (Critical)
Accelerometer mounted near free end, adhesive wax + tape
Beam coordinate system: x = beam length, y = vertical (dominant vibration), z = lateral
  Sensor axes are NOT aligned with beam axes (rotation + cross-talk). Use this mapping:
  beam_y (vertical) is mostly sensor_x (ax_V). Approx: sensor_x ≈ 0.95*beam_y + 0.10*beam_x
  beam_x leaks into sensor_y (ay_V). Approx: sensor_y ≈ 0.90*beam_x − 0.20*beam_y
  sensor_z (az_V) mostly lateral noise; small leakage from beam_y

## Slide 3: Acquisition Settings (Cross-check timestamps!)
DAQ configured: Fs = 10,000 Hz (nominal), 16-bit ADC
  IMPORTANT: Use the CSV timestamps to infer the true Fs; do not trust nominal Fs blindly.
Anti-alias filter: 2 kHz low-pass (analog)
Record length: ~12.5 s

## Slide 4: Excitation & Processing Guidance
Impact occurs near t ≈ 1.0 s (ringdown afterwards)
  For FFT/half-power, gate/window the ringdown segment (exclude pre-impact noise).
  Suggested window: start shortly after impact peak; end when amplitude approaches noise floor.
  Report how the gate was chosen.

## Slide 5: Sanity Checks & Expected Reporting
Convert volts → g → m/s² using sensor_calibration.txt
  Check that damping from log decrement and half-power are consistent (within ~0.02 absolute).
  If methods disagree, flag mode as FAIL and explain likely reasons.
Output must be a single CSV named modal_gtfa.csv (see benchmark prompt).