## Slide 1: Rig Notes: Vibration Test (Synthetic Benchmark)
Test type: impact/ringdown on a cantilever-like structure mounted to a rigid fixture
Objective: estimate the first 3 modal frequencies and damping ratios
  Methods: (i) logarithmic decrement (time domain) and (ii) half-power bandwidth (frequency domain)

## Slide 2: Sensor Mounting & Axis Mapping
Accelerometer mounted near free end, adhesive wax + tape
Beam axes: x = length, y = vertical bending (dominant), z = lateral
  Sensor axes are misaligned with beam axes (rotation + cross-talk). Use the proxy rule below.
  Proxy rule (required): analyze beam vertical motion using sensor x channel only: ax_V
  Do NOT reconstruct a beam-axis signal from multiple channels for this benchmark.

## Slide 3: Acquisition Settings (Cross-check timestamps!)
DAQ nominal configuration: Fs = 10,000 Hz (nominal), 16-bit ADC
  Required: infer the actual Fs from CSV timestamps; use Fs = 1/median(Δt).
Analog anti-alias filter: ~2 kHz low-pass (2-pole)
Record length: ~12.5 s

## Slide 4: Excitation & Processing Guidance
Impact occurs near t ≈ 1.0 s; ringdown afterwards
  For FFT/half-power, gate/window the ringdown segment (exclude pre-impact noise).
  Report the gate interval and window type used.

## Slide 5: Analysis Protocol (Deterministic, Required)
This slide fixes ambiguity so results are reproducible.
  Axis: use ax_V only (beam_vertical proxy).
  Fs: compute from timestamps: Fs = 1/median(Δt).
  Impact time: t_impact = timestamp at max(|a(t)|) after unit conversion.
  Gate: t_start = t_impact + 0.01 s; t_end = min(t_impact + 4.0 s, end).
  Pre-FFT: subtract mean of gated segment; apply Hann window.
  Mode search band: 20–400 Hz.
  Peak-pick: local maxima; sort by increasing f; require ≥20 Hz separation; keep first 3.
  f_n_hz_fft: use peak-bin frequency (no interpolation).
  Half-power: f1,f2 where magnitude first falls to Amax/√2; ζ_hp=(f2-f1)/(2 f_n).
  Log-decay: band-pass [f_n−15, f_n+15] Hz (4th-order Butterworth).
  Peaks: on |filtered|; ignore <5% of max; use first 10 peaks.
  f_n_hz_time: 1 / mean peak spacing; ζ_logdec from first vs last peak.
  k_eff: set NaN unless modal/effective mass is explicitly provided.

## Slide 6: Output Expectations
Return modal_gtfa.csv (3 rows: modes 1–3) and analysis_notes.txt
  analysis_notes.txt should record: axis_used, sampling_rate_hz, ringdown_gate_s, k_eff_status.
  If time- and freq-domain damping disagree by >0.02, mark verdict=fail and explain.